# Signal Hound VSG25 - Modification for better frequency stability

Signal Hound VSG25 - Disassembled
Signal Hound VSG25 - Modification Closeup
Signal Hound VSG25 - Mod Schematic
Signal Hound VSG25 - Mod Layout
## Tests
- Tests run at 162MHz nominal with 0dBm output power. Ambient Temp: 24C Deg
- VCTCXO Freq is measured by Racal 2202R Universal Counter/Timer (it has a rubidium reference so it is reliable!)
- Frequency drifting before modifications were over 500Hz
- Frequency drifting after VCTCXO modification was 19Hz
  - Initial freq: 162.000006MHz
  - After 2.5hrs: 162.000025MHz and kept drifting
- Frequency drifting after VCTCXO and heatsink added was 10Hz and stabilized relatively quickly
  - Initial freq: 161.999983MHz
  - After an hour frequency stabilised on 161.999993MHz